## Slide 1: Diffusion Weighted MRS: Experimental Design, Acquisition, Pre-Processing & Analysis
Itamar Ronen, PhD
C. J. Gorter Center for High Field MRI Department of Radiology
Leiden University Medical Center

## Slide 2: Synopsis
Why DW-MRS and what are we measuring?
The DW-MRS toolkit (1): pulse sequences
Unique microstructural information derived from DW-MRS
The DW-MRS toolkit (2): the essentials of DW-MRS preprocessing
Clinical applications and considerations for clinical DW-MRS protocols
Summary and a couple of recommendations

## Slide 3: Magnetic Resonance Spectroscopy – a window to brain neurochemistry (in the mM range)

## Slide 4: compartment- and cell-type specific probes of cellular microstructure through diffusion
Cho, Ins
astrocyte
NAA, Glu
neuron
Cellular morphology.
Viscosity and tortuosity.
Cytosolic streaming.
Intracellular structures.
Sub-compartmentalization.
Enzymatic processes.
Intra/extracellular distribution.

## Slide 5: DW-MRS toolbox (1) : pulse sequences (stimulated echo)
Diffusion time Δ coupled to tm, suitable for exploration of diffusion at long Δ (T1(metab) >> T2(metab))
Gradient duration δ coupled to TEmin
BP-STEAM generates less eddy currents and cross-terms with background/sequence gradients are minimized
BP-STEAM has longer TEmin, higher SAR and more chances for parasitic STEs
BP-STEAM easily converted to double diffusion encoding (DDE) sequence.
BP-DW-STEAM
DW-STEAM
Najac C. et al., Neuroimage 2014

## Slide 6: DW-MRS toolbox (1) : pulse sequences (spin echo)
Full SNR for given TE
Δ coupled to TE, limited by T2(metab)
BP versions use more available time for gdiff (more efficient)
Other advantages of BP retained
Easily transformed into DDE
BP-DW-PRESS
BP-isoDW-LASER
BP-sLASER

## Slide 7: Microstructural example (1)
G(parallel)
G(perpendicular)
01-08-2018
D||> D⊥ from a certain td onwards
decreases with td
(td→∞) ≈ 1/3 (td→0)
Fiber diameter ≈ 80μm, and from data ≈ 20μm. Mytochodrial contribution? Other structural restrictions?
td
tm = 0.075s

## Slide 8: Microstructural example (2): Are brain metabolites mostly contained in “fibers” (open-ended geometry) or in “cell bodies” (closed geometry)?
Strong time dependence only at very short td
No evidence for small, closed compartments in mouse, macaque or human cerebrum.
Najac C. et al., Neuroimage 2014
Najac C. et al., Brain Struct Func 2014
Valette J. et al., Front Neurosci 2018

## Slide 9: Microstructural example (3): anisotropic diffusion of metabolites in the corpus callosum
gpar.
gperp.
Astrocyte (tCho)
Axons (tNAA)

## Slide 10: Strong macroscopic anisotropy for the axonal metabolite NAA, much less for tCr and tCho
Strong effect of macroscopic anisotropy
Differentiation between cell types
Allows inference also on distribution of metabolites across cell types
tNAA
tCr
tCho
Ronen et al., Frontiers Integ. Neurosci 2013
Ronen et al., Brain Struct Func 2013

## Slide 11: Modeling the DWS(NAA) data yields: D(cytosol) of NAA and axonal orientation dispersion
Simple model with 2 (physically relevant) fitting variables
Integration of DWI and DWS in a common framework, each plays to its strength
Dcyto(NAA) strongly reflects the tortuosity of the cytosol: modulated by disease?
Ronen I. et al., Brain Struct Func 2014
Histological validation of σ(ϕ)
DTI collection to generate ê1 map
P(θ) between ê1 and gdiff
cylinders at macro-angles P(θ) with gdiff + microscopic fiber orientation dispersion p(ϕ)
Two variable model: Dcyto(NAA) and σ(ϕ), an extimate of the FOD.

## Slide 12: Macroscopic vs. microscopic anisotropy: telling them apart
In DWI, resolution is high enough for locally high macroFA.
VOI(DW-MRS)>>VoxelDWI
MacroFA highly affected by crossing fibers, fiber curvature, thus highly biased.
Makes sense to exploit DW-MRS for microstructural investigations while minimizing the effect of MacroFA.
Lasič, S. et al., Front. Phys. 2014
Szczepankiewicz et al, Neuroimage 2015

## Slide 13: Microscopic anisotropy (1): fully dispersed neurite model for NAA in white matter
Deviation from monoexponential fully explained by orientation dispersion.
Full dispersion achieved by “powder averaging”: averaging S(b) over multiple directions.
Yablonskiy DA et al., PNAS 2002
Lundell et al. in proc. ISMRM 2017, in preparation
5 b values
12 directions

## Slide 14: Microscopic anisotropy (2): Double diffusion encoding (DDE)
DDE picks up microscopic anisotropy also when there is no macroscopic one.
Dir(g1) is constant, Dir(g2) samples a circle that includes Dir(g1).
Anisotropic structures give rise to cos2θ modulation.
μFA can be extracted
G(d1)
G(d2)
θ
S(θ)
θ
S(θ)
Mitra P. Phys Rev B. 1995, Shemesh N. et al., Magn Reson Med 2016

## Slide 15: Microscopic anisotropy (2): DDE MRS neuronal and glial metabolites
“For NAA, the minima suggest a highly eccentric pore, occurring below diameters of 1.5 μm (the absolute minimum was d = 0.1 μm and D0 = 0.51 μm2/ms)”
Shemesh, N. et al., PLOS One 2017
Lundell et al. in proc. ISMRM 2018

## Slide 16: The DW-MRS toolkit (2): the essentials of data pre-processing
DW-MRS: a minefield of artifacts:
Bulk motion during diffusion sensitization period
Eddy currents
Gradient side bands
Quantification artifacts (MM baseline)
Usable spectra: 29/40
Usable spectra: 16/40
Genovese G. et al., Proc. ISMRM 2018
Eddy current correction:
Different for each DW condition
Separate acquisition of water spectra or from residual water peak
Caveat: Dwater>Dmetab
No ECC
ECC

## Slide 17: DW-MRS: disease models and development/ageing
Stroke (rodents, humans)
Brain tumors (rodents, humans)
Schizophrenia, bipolar disorder
Multiple sclerosis
Huntington’s disease
(Neuropsychiatric) systemic lupus erythematosus
Normal aging
Branzoli et al., Proc. ISMRM 2017
Wood et al., J Neurosci 2012
FA
MD
Ercan et al., Brain 2016
Adanyeguh et al., Proc. ISMRM 2018

## Slide 18: Clinical applications of DW-MRS: challenges and considerations
Low SNR (longer TE to accommodate gradients, DW signal loss).
Adequate informative DW-MRS protocols in a clinically-relevant time frame.
    What type of information? (ADC, μFA)
    What is the number of DW conditions (b values, directions) needed?
    How many repeats? TR?
Error propagation to all calculated measures
    Analytical calculation/Montecarlo simulation
    Proper setting of diffusion weighting conditions (number and values of b, gradient directions)
  Power calculation
b (s/mm2)
S.D. (a.u)
D=1.5μm2/ms
bopt=7400 s/mm2
Everything else being equal:
σ(ADC)b=2500:σ(ADC)b=7400 = 1.7
σ(ADC)b=1000:σ(ADC)b=7400 = 3.7

## Slide 19: DW-MRS: example power calculation
ADC(tNAA) from 3 orthogonal directions, 2 or 3 b values up to 3300 s/mm2
3T MRI scanner (Prisma Siemens), sLASER, TE=120ms, TR=3cs
Full acquisition time (3 b values): 14 minutes. With 2 b values: 10 minutes.
~20 subjects per group in a case/control experiment requiring 10% detectable difference in ADC(tNAA) at standard significance/power requirements.
α = 0.05, 1 – β = 0.80

## Slide 20: Summary and some humble suggestions
DW-MRS provides microstructural information unique in its compartmental specificity.
DW-MRS is complementary to less specific, more sensitive modalities.
DW-MRS does not exist as a product (talk to your vendor!)
Complex pipeline, requires strict quality control at every stage.
Experimental planning is crucial (type of information, error propagation, power analysis, clinical limitations).
Please don’t hesitate to find a DW-MRS expert to consult with and collaborate. We’re glad to help!

## Slide 21: DW-MRS geography, 1990-present

## Slide 22: ESMRMB Lectures on MR: Diffusion weighted MRS
October 10-12, 2018 Paris/FR Course Venue ICM - Institut du Cerveau et de la Moelle épinière Hôpital Pitié-Salpêtrière Paris/FR Course Organisers Francesca Branzoli Center for neuroimaging research (CENIR) – ICM Paris/FR Itamar Ronen C.J. Gorter Center for High Field MRI Leiden University Medical Center Leiden/NL Julien Valette Molecular Imaging Research Center Commissariat à l'énergie atomique et aux énergies alternatives (CEA) Fontenay-aux-Roses/FR

## Slide 23: Leiden, Leiden University, LUMC
Thank you very much!