## Slide 1: ESG 2024 Open Source Challenge:
Philipp Amrein, Feng Jia, Maxim Zaitsev
and Sebastian Littin
Medical Physics, University Medical Center Freiburg, Germany
Singapore, May 7th, 2024

## Slide 2
Speaker Name: Dr. Sebastian Littin
I have no financial interests or relationships to disclose with regard to the subject matter of this presentation.
Declaration of Financial Interests or Relationships

## Slide 3: Gradient Coil Design
Basic properties:
  Current carrying surface(s)
  Target
  Main field (B0) direction
Optimize the surface current density indirectly, using the Stream function :
Derive discretely realizable wire paths using stream lines
So far: Extensive manual post processing required to interconnect streamlines
Mesh
Iso Contours

## Slide 4: Openly Available Software Repositories
Fully flexible design and post processing “CoilGen: Open Source MR Coil Layout Generator“ [1]
Matlab: https://github.com/Philipp-MR/CoilGen
Python: https://github.com/kev-m/pyCoilGen
Python based “GradientDesignTool” (Patrick Fuchs) [2]
https://github.com/LUMC-LowFieldMRI/GradientDesignTool
Educational “Thin-wire approximation” [3]
https://github.com/Sebastian-MR/ThinWire_MRIGradientCoilDesign
Matlab based “CoilDesign” (Gale Bringout)
https://github.com/gBringout/CoilDesign/
[1] Amrein P et al CoilGen: Open-source MR coil layout generator. Magn Reson Med. 2022; 88( 3): 1465- 1479. doi:10.1002/mrm.29294
[2] De Vos et al. (2020 )IEEE Trans. Magn: Gradient Coil Design and Realization for a Halbach-Based MRI System. doi:10.1109/TMAG.2019.2958561
[3] Littin S et al (2021) Methods: Of Stream Functions and Thin Wires: An Intuitive Approach to Gradient Coil Design. Front. Phys. 9:699468. doi:10.3389/fphy.2021.699468

## Slide 5: Features of CoilGen
Generate triangular surface mesh
Design on arbitrary surfaces
Optimize the stream function on boundary elements of a mesh [4,5]
Advanced post-processing options
Output:
  Non-overlapping, interconnected coil layout
  .stl file for CAD import
  Dual layer path for PCBs
[4] Peeren G N. Stream function approach for determining optimal surface currents Journal of Computational Physics. 2003;191:305–321.
[5] Lemdiasov et al. A stream function method for gradient coil design Concepts in Magnetic Resonance Part B: Magnetic Resonance Engineering. 2005;26B:67–80.

## Slide 6: CoilGen: Beyond Stream Functions
Project on 2D surface, discretize
Analyze topology, define path
Interconnect in & between groups
Project back, manage overlaps

## Slide 7: CoilGen: Coil Designs for Halbach Systems
x-Gradient
y-Gradient
z-Gradient

## Slide 8: CoilGen: 3D printed carrier
Images courtesy of Nils Allek (FH Dortmund)
ISMRM 2024: 4080; Samardzija et al. „MRI4ALL Hackathon: Under a Week Build of Open-Source Gradient Coils for a Low-Field MRI”

## Slide 9: CoilGen: Printed Circuit Boards (PCBs)
Amrein et al. Optimal bi-planar gradient coil configurations for diamnond nitrogen-vacancy based diffusion-weighted NMR experiments, MagnResonMaterPhy
OCRA Gradients (M. Prier)

## Slide 10: CoilGen Post Processing: SVD Shim Coil
Jia et al, Design of a shim coil array matched to the human brain anatomy MRM 28016

## Slide 11: ezyMRI Workshop 2024: Gradient Design
Import wirepath
Subtract wirepath from cylinder
Section for printing
Coil Design
3 channels designed by different persons using CoilGen
3D objects designed in Blender

## Slide 12: ezyMRI Workshop 2024: Gradient Building
PGPA: Parallel Gradient Printer Array

## Slide 13: CoilGen Summary
Features
Design suite
  Target mesh generation/ mesh import
  Optmize Stream Function
  Derive discrete wire paths
Advanced post processing
  Topological analysis
  Interconnect stream lines
  Manage and reduce effects from return paths
Export 3D object
Benefits
Significantly speeds coil design
Enables rapid prototyping of shim and gradient coils
Available in MATLAB and Python

## Slide 14
Acknowledgements
All current and previous colleagues and collaboration partners:
Philipp Amrein
Feng Jia
Maxim Zaitsev
ezyMRI Team “Gradient Coil”
Everybody sharing his code
Funding sources
This work is part of the A4IM project.
This project (22HLT02 A4IM) has received funding from the European Partnership on Metrology, co-financed from the European Union‘s Horizon Europe Research and Innovation Programme and by the Participating States.
HORIZON-WIDERA-2021-ACCESS-03 MRITwins